## Slide 1: Gas-phase sulfuric acid in the stratosphere: measurement technique, previous and future observations Hans Schlager1 & Frank Arnold1,2 1DLR-Institut für Physik der Atmosphäre Oberpfaffenhofen 2Max-Planck-Institut für Kernphysik, Heidelberg
SSiRC Workshop
28-30 Oct 2013
Atlanta, GA, USA

## Slide 2: Background
Gasphase H2SO4 is an important compound of the stratospheric sulfur budget, however, data is sparse
Main H2SO4 sources gases are COS and SO2
H2SO4 abundance in the stratosphere is variable mainly due to seasonal temperature changes and variable SO2 input from volcanic eruptions
In-situ measurements of H2SO4 in the stratosphere are difficult to perform due low mixing ratios (sub-pptv) and sampling issues.
No in-situ H2SO4 data collected since late 80s.

## Slide 3: H2SO4 Profile (volcanic quiescent period)
(H2SO4 profiles: Christoph Brühl, MPI Mainz)
Log(p/hPa)
-14 -12 -10 -8
Main controlling factors of
gasphase H2SO4
10
20
30
40
50
60
70
km
VMR (48°N, Apr 2007)
Equilibrium saturation pressure of
H2SO4 vapor over H2SO4 – H2O
aerosol solution droplets
Photochemical H2SO4 production by
COS and SO2 oxidation initiated by
reaction with OH and heterogeneous
removal
H2SO4 production by COS photolysis
and reaction with O(3P) and loss by
photolysis and heterogeneous
removal due to meteor smoke
stronger
H2SO4
photolysis
removal
by meteor
smoke

## Slide 4: H2SO4 Profiles (mid-latitudes and tropics)
(Courtesy: Christoph Brühl, MPI Mainz)
VMR (2°N, Apr 2007)
Log(p/hPa)
-14 -12 -10 -8
10
20
30
40
50
60
70
km
VMR (48°N, Apr 2007)
-14 -12 -10 -8
Lower VMR
due to lower
temperatues

## Slide 5: H2SO4 Profiles (volcanic quiescent & unrest periods)
(Courtesy: Christoph Brühl, MPI Mainz)
VMR (48°N, Apr 2007)
VMR (48°N, Apr 1992/93)
-14 -12 -10 -8
Log(p/hPa)
-14 -12 -10 -8
10
20
30
40
50
60
70
km

## Slide 6: In-situ H2SO4 Measurement Technique: Active and Passive CIMS
CIMS reaction:
NO3-(HNO3)h(H2O)n + H2SO4 -> HSO4-(HNO3)l(H2O)m
+ (h-l+1) HNO3 + (n-m) H2O
[H2SO4] = (1/ k tr ) ln(1-R), R= HSO4-/NO3- cluster ions
ACIMS: NO3- ions produced by an ion source
PACIMS: NO3- produced in ambient air by cosmic rays
k(h=0-2) measured by Viggiano et al (1997): 2.3 – 1.7
x 10-9 cm3/s
tr: drift time in reaction cell (ACIMS) or
ion-ion recombination lifetime (PACIMS)

## Slide 7: H2SO4 CIMS measurements:
PBL (ACIMS): Eisele & Tanner (1993), Berresheim et al. (2000), Fiedler et al. (2005), Petäjä et al. (2009), Aufmhoff et al. (2010), Zheng et al. (2011)
TP layer (PACIMS) Möhler & Arnold (1992)
STR (PACIMS): Arnold & Fabian (1980), Arnold & Bührke 1983), Viggiano et al. (1983), Schlager et al. (1987)

## Slide 8: Passive CIMS: Negative Ion Chemistry
Life time / s

## Slide 9: Passive CIMS: Ion-Ion-Recombination Lifetime
Altitude / km
Lifetime / s
from ion density
measurements
and calculated
recommbination
coefficients

## Slide 10: Passive CIMS: Negative Ion Mass Spectrum
HSO4-(H2SO4)
HSO4-(H2SO4)2
HSO4-(H2SO4)3
NO3-(HNO3)
HSO4-(H2SO4)4

## Slide 11: Passive CIMS: Measured H2SO4 Profiles
B
M
(Schlager et al., 1987)
no re-evaporation
no photolysis
re-evaporation,
photolysis,
removal by
Meteor smoke
re-evaporation,
photolysis,
B
M

## Slide 12: Temperatures 30 hPa (Radiosonde data)
B
M

## Slide 13: Signature of El Chichon Eruption
(Arnold & Bührke, Nature 1983)

## Slide 14: StratoClim: H2SO4 measurements on board the Geophysica
Tentative schedule:
Test campaign 2015
South-East Asia campaign 2016

## Slide 15
Challenges of H2SO4 measurements on board Geophysica
To achieve a detection limit of 10 ppqv (use of LNe cryopump)
To calibration H2SO4 wall losses in the instrument sampling line
To avoid aerosol evaporation in the sampling line
To prepare automatic operation and in-flight calibration
StratoClim measurements will provide first H2SO4 data in
the stratosphere since more than 25 years!